## Slide 1
8 核远程写入版 AllGather：算子执行流程
八个核心同时启动同一个 collective operator；每个源分片写入其他 7 个核心的远程接收槽位
核心语义
Y_j[i] = X_i
目标核 j 的第 i 个接收槽位
AllGather = 搬运 + 拼接，不做数值相加
C = S / 8
CORE
LAUNCH
LOCAL
OWN SLOT
REMOTE WRITE / NoC
ORDER + FLAG
WAIT
LOCAL OUTPUT
Core 0
start AllGather
X0 [C]
Y0[0] = X0
remote_write: X0 → Yj[0] j ≠ 0 · 7 × put
fence → ready_j[0]
wait ready_0[0:8]
Y0 = [X0, X1, …, X7]
→
→
→
→
→
→
→
Core 1
start AllGather
X1 [C]
Y1[1] = X1
remote_write: X1 → Yj[1] j ≠ 1 · 7 × put
fence → ready_j[1]
wait ready_1[0:8]
Y1 = [X0, X1, …, X7]
→
→
→
→
→
→
→
Core 2
start AllGather
X2 [C]
Y2[2] = X2
remote_write: X2 → Yj[2] j ≠ 2 · 7 × put
fence → ready_j[2]
wait ready_2[0:8]
Y2 = [X0, X1, …, X7]
→
→
→
→
→
→
→
Core 3
start AllGather
X3 [C]
Y3[3] = X3
remote_write: X3 → Yj[3] j ≠ 3 · 7 × put
fence → ready_j[3]
wait ready_3[0:8]
Y3 = [X0, X1, …, X7]
→
→
→
→
→
→
→
Core 4
start AllGather
X4 [C]
Y4[4] = X4
remote_write: X4 → Yj[4] j ≠ 4 · 7 × put
fence → ready_j[4]
wait ready_4[0:8]
Y4 = [X0, X1, …, X7]
→
→
→
→
→
→
→
Core 5
start AllGather
X5 [C]
Y5[5] = X5
remote_write: X5 → Yj[5] j ≠ 5 · 7 × put
fence → ready_j[5]
wait ready_5[0:8]
Y5 = [X0, X1, …, X7]
→
→
→
→
→
→
→
Core 6
start AllGather
X6 [C]
Y6[6] = X6
remote_write: X6 → Yj[6] j ≠ 6 · 7 × put
fence → ready_j[6]
wait ready_6[0:8]
Y6 = [X0, X1, …, X7]
→
→
→
→
→
→
→
Core 7
start AllGather
X7 [C]
Y7[7] = X7
remote_write: X7 → Yj[7] j ≠ 7 · 7 × put
fence → ready_j[7]
wait ready_7[0:8]
Y7 = [X0, X1, …, X7]
→
→
→
→
→
→
→
最终：Y0 = Y1 = … = Y7 = [X0, X1, …, X7]
每核：7×C 发送 + 7×C 接收；全系统 56×C = 7S
硬件最小能力：remote DMA / NoC + 远程地址偏移 + 写入顺序/fence + completion flag；无需 Reduce Engine
AllGather remote-write flow · 8 cores · editable diagram